## Slide 1: FSAE Tire Temperature Visualization
ECE3220 Final Project
Marshall Lindsay
Max Houck

## Slide 2: Background Information

## Slide 3: The Vision

## Slide 4: Printing Filled Rectangles
Windows.h
RECT – left, right, top, bottom
HBRUSH (SolidBrush)
RGB(red, green, blue)
FillRect

## Slide 5: Linear Interpolation of Data Points
Solid colors are nice, but lack detail.
  What is the temperature between the different points?
Solution: Interpolate data points between the measured locations.
  Linear interpolation.
    Y = mX + b where m = (y1 – y2)/(x1 – x2)
  Quadradic interpolation
    Y = a(x-h)^2 + c where ‘h’ is the x offset and ‘a’ scales the rate

## Slide 6: Linear Interpolation Between 2 Points
RED = -RGB + 255
BLUE = RGB
Color(true RGB) = (RED, 0, BLUE)
Pros:
Nice gradient between points
Covers “hot” and “cold” conditions
Cons:
Lacks color
  No one wants a 2 color heat map!

## Slide 7: 1020 RGB Linear Interpolation
3 colors (Red, Green, Blue) each with a range of 255 –>
1020 different values (Assuming start condition of max blue and end condition of max red).
Pros:
Lots of color.
Not only hot and cold but warm
Cons:
No color between heat zones
  Hot? Cold?
No gradient

## Slide 8: 510 RGB Linear Interpolation
Cut the number of RGB values in half.
Pros:
Lots of color and color variants
  Easy to tell hot from cold from warm
Great looking gradient between colors
Cons:
None.

## Slide 9: 510 Quadratic RGB Interpolation

## Slide 10: RGB Gradient Given 3 Celsius Values
Problems
  510 gradient assumes constant gradient between all 3 points.
    3 Celsius values are (assumed to be) random at any point in time. Therefore the slope between any two points is also random.
  Conversion between Celsius and RGB
    Converting from RGB to “true” RGB from graphs and equations

## Slide 11: Celsius to RGB Conversion
  Assumptions:
    Max degree Celsius – 110
    Min degree Celsius – 0
  510 Linear RGB Interpolation
    RGB = (Scaling Factor)(Degree C)
    Scaling Factor is a ratio
    Scaling Factor = #RGB values / #Possible Degree C = 510 / 110

## Slide 12: Celsius to RGB Conversion
‘RGB’
RealRGB

## Slide 13: RGB Gradient – 3 Celsius Values